# Appendix P. ISP download sample program for STC8H series MCU using third-party MCU
## P.1. Power control reference circuit
STC chip ISP download requires hardware reset of the target to enter ISP download mode. When using a third-party MCU to download the ISP of the STC chip, it is recommended to use the following power control circuit to achieve.

22u

0.1u
471

Target chip
power supply
MCU_Vcc

SS8550

2k

Power
control pin
External
power input
## P.2. Communication protocol flowchart
Serial port initialization / Start / Handshake / Setting parameters / Ready to program / Erase flash / Write user code / Finish / Overall process	Command header: 4 bytes / [46H B9H 6AH 00H] / Packet length: 1 byte / excluding 46H and B9H / Command byte: 1 byte / Command parameters / Packet checksum: 2 bytes / End of command: 1 byte / [16H] / Send packet / excluding 46H and B9H	[46H B9H 68H 00H] / [16H] / Receive packet / Command header: 4 bytes / Packet length: 1 byte / excluding 46H and B9H / Command byte: 1 byte / Command parameters / Packet checksum: 2 bytes / excluding 46H and B9H / End of command: 1 byte
Set minimum baud rate / (recommended is 2400) / Set even parity mode / Set 8 data bits / Serial port / initialization / End of module / Set 1 stop bit / Send 7FH / Handshake / Complete packet / received? / N / Y / End of module	Send packet / Setting parameters / N / Y / Set command parameters: / Parameter 1: 00H / Is received data / correct? / Y / Error handling / N / The reload count sets / the maximum baud / rate of the serial port. / Refer to the serial port / chapter for the / calculation method of / the timer's reload count. / Set the maximum baud / rate of the serial port / Parameter 2: 00H / Parameter 5: 00H / Parameter 6: 00H / Parameter 7: 00H / 3: reload count high byte / 4: reload count low byte / Complete packet / received? / End of module / Set command byte: 01H	Write user code / N / Y / Y / N / Y / Code download / complete? / N / End of module / Error handling / Is received data / correct? / Send packet / Complete packet / received? / Set command parameters: / 1: target address high byte / 2: target address low byte / Parameter 3: 5AH / Parameter 4: A5H / Set command byte: 22H / Parameter 5: code byte 1 / Parameter 6: code byte 2 / ... / Set command byte: 02H
Erase Flash / N / Y / Y / N / End of module / Error handling / Is received data / correct? / Send packet / Complete packet / received? / Set command byte: 03H / Set command parameters: / Parameter 1: 00H / Parameter 2: 00H / Parameter 3: 5AH / Parameter 4: A5H	Ready to program / N / Y / Y / N / End of module / Error handling / Is received data / correct? / Send packet / Complete packet / received? / Set command byte: 05H / Set command parameters: / Parameter 1: 00H / Parameter 2: 00H / Parameter 3: 5AH / Parameter 4: A5H

## P.3. Reference code (C language)
// Note: When using this code to download the STC8H series MCU, the target
// chip must be powered on after the Download code is executed, otherwise
// the target chip will not be able to download correctly.

#include "stc8h.h"

typedef bit BOOL;
typedef unsigned char BYTE;
typedef unsigned short WORD;

// macro, constant definition
#define FALSE 0
#define TRUE 1
#define LOBYTE(w) ((BYTE)(WORD)(w))
#define HIBYTE(w) ((BYTE)((WORD)(w) >> 8))

#define MINBAUD 2400L
#define MAXBAUD 115200L

#define FOSC 11059200L // Operating frequency of main control chip.
#define BR(n) (65536 - (FOSC/(n)+2) /4) // The formula for calculating the baud rate
        // of the serial port of the main control chip.
        // The addition of 2 is to make the Keil compiler
        // automatically realize the rounding operation.
#define T1MS (65536 - FOSC/1000) // Main control chip 1ms timing initial value

#define FUSER 24000000L // STC8H series target chip operating frequency.
#define RL(n) (65536 - (FUSER/(n)+2) /4) // STC8H series target chip serial port baud rate
        // calculation formula.
        // The addition of 2 is to make the Keil compiler
        // automatically realize the rounding operation.

// Variable definitions
BOOL f1ms; // 1ms flag bit
BOOL UartBusy; // Serial port sending busy flag
BOOL UartReceived; // Serial port data receiving complete flag bit
BYTE UartRecvStep; // Serial port data receiving control
BYTE TimeOut; // Serial communication timeout counter
BYTE xdata TxBuffer[256]; // Serial data send buffer
BYTE xdata RxBuffer[256]; // Serial data receiving buffer
char code DEMO[256]; // demo code data

// function declaration
void Initial(void);
void DelayXms(WORD x);
BYTE UartSend(BYTE dat);
void CommInit(void);
void CommSend(BYTE size);
BOOL Download(BYTE *pdat, long size);

// main function entry
void main(void) {
    P3M0 = 0x00;
    P3M1 = 0x00;
    Initial();

    if (Download(DEMO, 256)) {
        // download successful
        P3 = 0xff;
        DelayXms(500);
        P3 = 0x00;
        DelayXms(500);
        P3 = 0xff;
        DelayXms(500);
        P3 = 0x00;
        DelayXms(500);
        P3 = 0xff;
        DelayXms(500);
        P3 = 0x00;
        DelayXms(500);
        P3 = 0xff;
    } else {
        // download failed
        P3 = 0xff;
        DelayXms(500);
        P3 = 0xf3;
        DelayXms(500);
        P3 = 0xff;
        DelayXms(500);
        P3 = 0xf3;
        DelayXms(500);
        P3 = 0xff;
        DelayXms(500);
        P3 = 0xf3;
        DelayXms(500);
        P3 = 0xff;
    }

    while (1);
}

// 1ms Timer Interrupt Service Routine
void tm0(void) interrupt 1 {
    static BYTE Counter100;

    f1ms = TRUE;

    if (Counter100-- == 0) {
        Counter100 = 100;

        if (TimeOut)
        TimeOut--;
    }
}

// Serial Interrupt Service Routine
void uart(void) interrupt 4 {
    static WORD RecvSum;
    static BYTE RecvIndex;
    static BYTE RecvCount;
    BYTE dat;

    if (TI) {
        TI = 0;
        UartBusy = FALSE;
    }

    if (RI) {
        RI = 0;
        dat = SBUF;

        switch (UartRecvStep) {
        case 1:
        if (dat != 0xb9)
        goto L_CheckFirst;

        UartRecvStep++;
        break;

        case 2:
        if (dat != 0x68)
        goto L_CheckFirst;

        UartRecvStep++;
        break;

        case 3:
        if (dat != 0x00)
        goto L_CheckFirst;

        UartRecvStep++;
        break;

        case 4:
        RecvSum = 0x68 + dat;
        RecvCount = dat - 6;
        RecvIndex = 0;
        UartRecvStep++;
        break;

        case 5:
        RecvSum += dat;
        RxBuffer[RecvIndex++] = dat;

        if (RecvIndex == RecvCount)
        UartRecvStep++;
        break;

        case 6:
        if (dat != HIBYTE(RecvSum))
        goto L_CheckFirst;

        UartRecvStep++;
        break;

        case 7:
        if (dat != LOBYTE(RecvSum))
        goto L_CheckFirst;

        UartRecvStep++;
        break;

        case 8:
        if (dat != 0x16)
        goto L_CheckFirst;

        UartReceived = TRUE;
        UartRecvStep++;
        break;

        L_CheckFirst:
        case 0:
        default:
        CommInit();
        UartRecvStep = (dat == 0x46 ? 1 : 0);
        break;
        }
    }
}

// system initialization
void Initial(void) {
    UartBusy = FALSE;
    SCON = 0xd0; // Serial port data mode must be 8-bit data + 1 stop bit + even parity
    AUXR = 0xc0;
    TMOD = 0x00;
    TH0 = HIBYTE(T1MS);
    TL0 = LOBYTE(T1MS);
    TR0 = 1;
    TH1 = HIBYTE(BR(MINBAUD));
    TL1 = LOBYTE(BR(MINBAUD));
    TR1 = 1;
    ET0 = 1;
    ES = 1;
    EA = 1;
}

// Xms Delay program
void DelayXms(WORD x) {
    do {
        f1ms = FALSE;
        while (!f1ms);
    } while (x--);
}

// Serial data sending program
BYTE UartSend(BYTE dat) {
    while (UartBusy);
    UartBusy = TRUE;
    ACC = dat;
    TB8 = P;
    SBUF = ACC;

    return dat;
}

// Serial communication initialization
void CommInit(void) {
    UartRecvStep = 0;
    TimeOut = 20;
    UartReceived = FALSE;
}

// Send serial communication data packet
void CommSend(BYTE size) {
    WORD sum;
    BYTE i;
    UartSend(0x46);
    UartSend(0xb9);
    UartSend(0x6a);
    UartSend(0x00);
    sum = size + 6 + 0x6a;
    UartSend(size + 6);

    for (i=0; i<size; i++) {
        sum += UartSend(TxBuffer[i]);
    }

    UartSend(HIBYTE(sum));
    UartSend(LOBYTE(sum));
    UartSend(0x16);
    while (UartBusy);
    CommInit();
}

// ISP download program for STC15H series chips
BOOL Download(BYTE *pdat, long size) {
    BYTE arg;
    BYTE offset;
    BYTE cnt;
    WORD addr;

    // Handshake
    CommInit();

    while (1) {
        if (UartRecvStep == 0) {
        UartSend(0x7f);
        DelayXms(10);
        }

        if (UartReceived) {
        arg = RxBuffer[4];

        if (RxBuffer[0] == 0x50)
        break;

        return FALSE;
        }
    }

    // Set parameters (set the highest baud rate and waiting time from the chip)
    TxBuffer[0] = 0x01;
    TxBuffer[1] = arg;
    TxBuffer[2] = 0x40;
    TxBuffer[3] = HIBYTE(RL(MAXBAUD));
    TxBuffer[4] = LOBYTE(RL(MAXBAUD));
    TxBuffer[5] = 0x00;
    TxBuffer[6] = 0x00;
    TxBuffer[7] = 0x97;
    CommSend(8);

    while (1) {
        if (TimeOut == 0)
        return FALSE;

        if (UartReceived) {
        if (RxBuffer[0] == 0x01)
        break;

        return FALSE;
        }
    }

    // Prepare
    TH1 = HIBYTE(BR(MAXBAUD));
    TL1 = LOBYTE(BR(MAXBAUD));
    DelayXms(10);
    TxBuffer[0] = 0x05;
    TxBuffer[1] = 0x00;
    TxBuffer[2] = 0x00;
    TxBuffer[3] = 0x5a;
    TxBuffer[4] = 0xa5;
    CommSend(5);

    while (1) {
        if (TimeOut == 0)
        return FALSE;

        if (UartReceived) {
        if (RxBuffer[0] == 0x05)
        break;

        return FALSE;
        }
    }

    // erase
    DelayXms(10);
    TxBuffer[0] = 0x03;
    TxBuffer[1] = 0x00;
    TxBuffer[2] = 0x00;
    TxBuffer[3] = 0x5a;
    TxBuffer[4] = 0xa5;
    CommSend(5);
    TimeOut = 100;

    while (1) {
        if (TimeOut == 0)
        return FALSE;

        if (UartReceived) {
        if (RxBuffer[0] == 0x03)
        break;

        return FALSE;
        }
    }

    // write user code
    DelayXms(10);
    addr = 0;
    TxBuffer[0] = 0x22;
    TxBuffer[3] = 0x5a;
    TxBuffer[4] = 0xa5;
    offset = 5;

    while (addr < size) {
        TxBuffer[1] = HIBYTE(addr);
        TxBuffer[2] = LOBYTE(addr);
        cnt = 0;
        while (addr < size) {
        TxBuffer[cnt+offset] = pdat[addr];
        addr++;
        cnt++;
        if (cnt >= 128)
        break;
        }

        CommSend(cnt + offset);

        while (1) {
        if (TimeOut == 0)
        return FALSE;

        if (UartReceived) {
        if ((RxBuffer[0] == 0x02) && (RxBuffer[1] == 'T'))
        break;

        return FALSE;
        }
        }

        TxBuffer[0] = 0x02;
    }

    //// write hardware options
    //// If there is no need to modify the hardware options, this step
    //// can be skipped directly. At this time, all hardware options
    //// remain unchanged, and the frequency of the MCU is the frequency
    //// adjusted last time.
    //// If writing the hardware option, the internal IRC frequency of
    //// the MCU will be fixed at 24M, and other options will be restored
    //// to factory settings.
    //// Suggestion: Use the STC-ISP download software for the first time
    //// to set the hardware options of the slave chip and then use the
    //// master chip to download the program from the chip without writing
    //// the hardware options
    //DelayXms(10);
    //for (cnt=0; cnt<128; cnt++)
    //{
    // TxBuffer[cnt] = 0xff;
    //}
    //TxBuffer[0] = 0x04;
    //TxBuffer[1] = 0x00;
    //TxBuffer[2] = 0x00;
    //TxBuffer[3] = 0x5a;
    //TxBuffer[4] = 0xa5;
    //TxBuffer[33] = arg;
    //TxBuffer[34] = 0x00;
    //TxBuffer[35] = 0x01;
    //TxBuffer[41] = 0xbf;
    //TxBuffer[42] = 0xbd; // P5.4 is the IO port
    ////TxBuffer[42] = 0xad; // P5.4 is reset pin
    //TxBuffer[43] = 0xf7;
    //TxBuffer[44] = 0xff;
    //CommSend(45);
    //while (1) {
    // if (TimeOut == 0)
    // return FALSE;
    //
    // if (UartReceived) {
    // if ((RxBuffer[0] == 0x04) && (RxBuffer[1] == 'T'))
    // break;
    // return FALSE;
    // }
    //}

    // Download completed
    return TRUE;
}

char code DEMO[256] =
{
    0x80,0x00,0x75,0xB2,0xFF,0x75,0xB1,0x00,0x05,0xB0,0x11,0x0E,0x80,0xFA,0xD8,0xFE,
    0xD9,0xFC,0x22,
};